# Text boxes

PRIOR TO COMMENCING CIRCLE: Flaps App; Gear Down; App +10; Pwr 1.23 EPR/3800 PPH

45( for 30 secs (or 30( for 45 secs)

Check Winds

Check Displacement

1

2

3

4

Tail Wind Component:

0 Kts TW = 1 NM (or 15 Sec)

30Kts TW = Abeam the threshold

30( Bank; bottom rudder; add pwr (+.02/200#); level turn

G/S intercept = Flaps Landing

OBJECTIVE:  Wings level @ 1NM/300 Ft (but not later than 1/2 NM/200 Ft

5

6

7

8

ICAO:  Pilots must maintain visual contact with the “Runway Environment” (i.e., the runway threshold or approach lighting aids or other markings identifiable with the runway)

UNITED STATES:  The pilot is required to maintain visual contact with the airport environment

Diagram not to scale

Power settings based on level flight

User assumes responsibility for accuracy and currency

The Circling Approach

FOR TRAINING ONLY